# Volume control

The volume of the CORDA QUICKSTEP is also controlled by the dial on the front of the amp and is increased by clock-wise rotation. Volume incrase is not continuously but in 31 small steps.

If high-sensitive headphones or sources with a high output signal are used, then high sound levels are already reached at very low settings of the volume control. To refine control it is possible to reduce the gain factor of the amp. Just below the input socket a switch can be found. For low gain set this switch to its left-most position. For high gain choose the right-most position (default).

!! Please choose your volume setting with caution !!

The driving capabilities of the CORDA QUICKSTEP by far exceed that of a regular portable player. This not only guarantees less distortion, but also has the danger of severe hearing damage. While listening to headphones we lack several feedback mechanisms on volume level that are present when we listen to loudspeakers. Much less distortion, no feeling of the lower frequencies by our body and no psychological restraints not to annoy our fellow-men easily seduces us to listen at volume levels that are detrimental to our hearing. Hearing damage from regular exposure to high sound levels progresses slowly but is irreversible and can result in permanent hearing loss.

# Current Consumption

The amp by default has a current consumption of approximately 35 mA. The battery lifetime (alkaline) is around 20..25 hours. The amplifier also offers a mode of low current consumption of 20 mA which increases battery life to around 40 hours. Inside the amp a three pin connector allows to toggle between the two current consumption modes. Please place the shunt on tip of this connector to the position preferred as indicated on the PCB. Note that in low-current-consumption mode the sound quality is slightly reduced. With an external supply connected the amplifier automatically runs in high current consumption mode

# Technical data

Weight without battery:	115 gr.

### Measures:	8.8 x 6.5 x 2.2 cm

Supply voltage:	6 .. (9) .. 15 Volts DC

Mean current uptake:	20 / 35 mA (low/high current mode)

Maximal amplification (1 kHz):	-2 / 14 dB (low/high gain)

Input impedance:	120 / 17 kOhm (low/high gain)

Output impedance:	< 1 Ohm

CORDA QUICKSTEP

high-end portable headphone-amplifier

USER’S MANUAL

Dear music-lover,

The CORDA QUICKSTEP is a small portable amplifier, specially designed to drive headphones. It offers a sound quality and driving capabilities far beyond that of an ordinary headphone socket found on a portable player and thus allows you to exploit the full sonic potential of your phones.

To obtain the best possible results with your new headphone-amplifier, we ask you to read these instructions carefully. The CORDA QUICKSTEP was developed by music-lovers for music-lovers and we hope that it will serve you well for a long time.

Jan Meier

# Connection

The QUICKSTEP was designed to be used in combination with a portable music-player. Please connect the "line-out" socket of your player with the right input-socket on the front of your headamp. If your player doesn't have a "line-out" socket use its headphone-socket instead and turn its volume to maximum.

Your headphone should be connected to the output-socket on the left front side of the CORDA QUICKSTEP. This headphone socket is intended for 3.5 mm (1/8”) stereo plugs. If your headphone only has a 6.35 mm (1/4”) plug, then use an adapter that can be obtained in most electronics or audio shops. Please note that many headphones have a 3.5 mm plug (invisibly) integrated in their 6.5 mm plug. Consult the user manual of your headphone if in doubt.

Sonically the CORDA QUICKSTEP also sounds much better than most sockets found on home-units. You therefore may want to use this headamp in combination with your equipment at home. The best sonic performance is achieved if you connect the headamp directly to the source. For this you need an adapter cable that has a 3.5 mm stereo-plug at one side and two RCA-connectors at the other. Ask your local electronics or audio shop.

Note: The ground contact of the output socket carries an active signal. Therefore this output should never be connected to a passive ground. The QUICKSTEP  can not be used as a pre-amplifier! If in doubt, please contact Meier-Audio for advice.

# Power

The CORDA QUICKSTEP can be powered from a 9V block battery placed inside the battery compartment at the backside of the amp. The proper position and polarity of the battery are indicated at the backpanel.

The amp can also be powered from a external regulated powersupply with a current capacity of at least 100 mA and a DC voltage between 6 and 15 Volts. The supply is to be connected directly to the power supply jack at the backside of the amp.

If at the same time a battery is connected the amp will use the source with the highest voltage. It is therefore recommended to use a powersupply voltage of at least 10V as this will block/minimize battery current.

The inside/outside diameters of the power plug should be 1.3/3.5 mm (0.05”/0.14”). The outside shaft of the plug should have negative voltage. The inside should be positive. The amplifier is protected against supply voltages of reversed (false) polarity.

!! Applied voltages higher than 15V may damage your amp !!

!! Do not use an AC powersupply or an unregulated supply !!

For mechanical stability the door of the battery compartment is fully made of metal. As a result there is no “spring” action that keeps the door properly in place when no battery is inserted. Therefore we recommend to always keep a battery inserted, even when an external power supply is used. It will prevent you from loosing the door.

# Activation of the device

The CORDA QUICKSTEP is switched OFF by turning the volume-dial on the front of the amplifier to its most counter-clock-wise position. You should feel a mechanical “click”. Turning the dial clockwise will activate the amplifier. While switched ON the light on the front side will be lit.

While connected to an external supply the amplifier will be automatically turned ON.